## Slide 1: Modeling VNFs in a contrail environment
How to design a VNF using Contrail & Heat
Umberto Manferdini

## Slide 2
Where are we now?
What’s Heat?
Contrail and Heat: modeling VNFs
From vanilla Neutron to Juniper Contrail
Service Chaining

## Slide 3: Juniper contrail
Juniper SDN Controller
Manages virtual networking within the DC
Based on well known protocols and solutions like BGP and VPNs

## Slide 4: Originally it was a switched network

## Slide 5: Then data centers came

## Slide 6: Finally virtualization appeared
A network within a network
A network inside a server
Virtual Machines are the new appliances
Virtual Networks are the new switched networks

## Slide 7: Same thing…different objects
physical switch/router
virtual router

## Slide 8: Call for new models
Yesterday, we used cables to connect physical devices
Now, we have to connect virtual machines
We need new models to describe these new scenarios

## Slide 9: Virtualization brings automation
Virtualization is software
Software is more inclined to be automated
Virtualization opens to network automation

## Slide 10: Automation means heat
Openstack deploys and manage the DC
Openstack has tool for automation called Heat
Contrail fully integrates with Heat
Contrail provides its own Heat objects

## Slide 11: And heat means yaml
Heat is a built-in Openstack module
Heat uses YAML language
Easy to read and write

## Slide 12: Contrail has its own objects

## Slide 13: Automation through stacks
Heat creates stacks
Stacks are a list resources
Resources are virtual network, virtual machines, etc…

## Slide 14: What do I have to do?
New Virtual Network
Extend Virtual Network outside the DC
New Virtual Machine on a Virtual Network
Manage VLANS in a “v” environment

## Slide 15: From words to heat
Need to take an abstract input as request
For example “configure a virtual network”
And translate it into a Heat template

## Slide 16: What’s a heat template?
Structured YAML files
Template file, where we define resources
Environment file, where we assign values to parameters

## Slide 17: Objects for everyone
Openstack offers a wide range of Heat object
Nova objects
Glance objects
Contrail objects
…

## Slide 18: Inside a heat template
Heat templates made of multiple sections
Two main sections
Parameters section
Resource section

## Slide 19: Declaring parameters
heat_template_version: 2015-04-30
parameters:
myname :
type: string
default: ‘nameX’
myimage :
type: string
default: ‘ubuntu’
myflavor :
type: string
default: ‘smallvm’

## Slide 20: Declaring resources
resources:
test-net:
type: OS::Neutron::Net
properties:
name: ‘heat-net’
test-subnet:
type: OS::Neutron::Subnet
properties:
name: ‘heat-subnet’
network_id: { get_resource: test-net }
cidr: ‘192.168.1.0/16’
server1:
type: OS::Nova::Server
properties:
name: { get_param: myname }
image: { get_param: myimage }
flavor: { get_param: myflavor }
networks:
- network: { get_resource: test-net }
hardocded value
get_resource
get_param
resource type

## Slide 21: Environment file
Parameters defined in the template file
We need to give them a value
Environment file is for this!
parameters:
myname : Ubuntu-1
myimg : ubu14-iso
myflavor : linux-perf

## Slide 22: Who’s first?
Heat is smart
But not too smart
Some order is required
Use “depends_on” to manage it
server1:
type: OS::Nova::Server
depends_on [test-subnet, test-net]
properties:
name: { get_param: myname }
image: { get_param: myimage }
flavor: { get_param: myflavor }
networks:
- network: { get_resource: test-net }

## Slide 23
Virtual network
Virtual machine interface
Instance IP
BGPaaS
Sub-interfaces
Allowed address pair

## Slide 24: Contrail virtual networks
Key element in Contrail networking
Used to connect Virtual Machines

## Slide 25: Virtual network properties
Virtual Networks has a name
Reference an IPAM (Contrail wrapper for virtual networks)
resources:
vip_vn:
type: OS::ContrailV2::VirtualNetwork
properties:
name: ‘myvn’
network_ipam_refs: ['default-domain:default-project:default-network-ipam']

## Slide 26: Customizing the virtual network
Forwarding mode
RPF check
Flooding unknown unicast
VXLAN identifier
resources:
vip_vn:
type: OS::ContrailV2::VirtualNetwork
properties:
virtual_network_properties:
{
virtual_network_properties_forwarding_mode: ‘l3’,
virtual_network_properties_rpf: ‘enable’,
virtual_network_properties_vxlan_network_identifier: ‘1234’,
}
flood_unknown_unicast: ‘true’

## Slide 27: How do I ecmp?
Contrail supports ECMP
Up to 5 configurable fields
resources:
vip_vn:
type: OS::ContrailV2::VirtualNetwork
properties:
ecmp_hashing_include_fields:
{
ecmp_hashing_include_fields_destination_ip: ‘true’,
ecmp_hashing_include_fields_destination_port: ‘false’,
ecmp_hashing_include_fields_hashing_configured: ‘true’,
ecmp_hashing_include_fields_ip_protocol: ‘true’,
ecmp_hashing_include_fields_source_ip: ‘false’,
ecmp_hashing_include_fields_source_port: ‘false’,
}
port_security_enabled: ‘true’

## Slide 28: Creating subnets
Not a dedicated object
Network address and mask
Allocation pools
DHCP
Gateway
Allocation order

## Slide 29: Subnets in heat
resources:
vip_vn:
type: OS::ContrailV2::VirtualNetwork
properties:
network_ipam_refs_data:
[{
network_ipam_refs_data_ipam_subnets:
[{
network_ipam_refs_data_ipam_subnets_subnet:
{
network_ipam_refs_data_ipam_subnets_subnet_ip_prefix: '192.168.33.0',
network_ipam_refs_data_ipam_subnets_subnet_ip_prefix_len: '24',
},
network_ipam_refs_data_ipam_subnets_addr_from_start: 'true',
network_ipam_refs_data_ipam_subnets_default_gateway: '192.168.33.3',
network_ipam_refs_data_ipam_subnets_enable_dhcp: 'false',
network_ipam_refs_data_ipam_subnets_allocation_pools:
[{
network_ipam_refs_data_ipam_subnets_allocation_pools_start: '192.168.33.5',
network_ipam_refs_data_ipam_subnets_allocation_pools_end: '192.168.33.10',
}]
}]
}]

## Slide 30: Checking everything is alright

## Slide 31: Virtual nic
Virtual machine port
Connects VM to the Virtual Network
It is actually 2 objects
Virtual Machine Interface
Instance IP

## Slide 32: Virtual machine interface
Minimal configuration
Name
Virtual Network Reference
resources:
vmi_newnet:
type: OS::ContrailV2::VirtualMachineInterface
properties:
name: 'my_vmi'
virtual_network_refs: [{ list_join: [':', { get_attr: [ newnet_vn, fq_name ] } ] }]
Internal function
Fully Qualified Name
prepends “domain:project”

## Slide 33: Leveraging existing networks
Existing network
Simply pass the FQDN network name as a parameter
FQDN name means “domain:project:network”
vmi_prex:
type: OS::ContrailV2::VirtualMachineInterface
properties:
virtual_network_refs: [ {get_param: mgmt-net} ]
parameters:
mgmt-net: 'default-domain:admin:mgmt'
env
file

## Slide 34: I want my own mac
By default, Contrail automatically assigns a MAC to a port
Optionally, we can assign a custom MAC
resources:
vmi_newnet:
type: OS::ContrailV2::VirtualMachineInterface
properties:
virtual_machine_interface_mac_addresses:
{
virtual_machine_interface_mac_addresses_mac_address: [ ‘aa:bb:cc:dd:ee:ff’],
}

## Slide 35: A port needs an ip
Second element is the Instance IP
References a virtual networks
References a VMI
instanceip_1:
type: OS::ContrailV2::InstanceIp
depends_on: [ vmi_newnet, newnet_vn ]
properties:
virtual_machine_interface_refs: [{ get_resource: vmi_newnet }]
virtual_network_refs: [{ list_join: [':', { get_attr: [ newnet_vn, fq_name ] } ] }]

## Slide 36: My ip or your ip?
We can reference an existing virtual network
Or specify a fixed IP address
iip_fixed:
type: OS::ContrailV2::InstanceIp
depends_on: [ vmi_obj ]
properties:
virtual_machine_interface_refs: [{ get_resource: vmi_obj }]
virtual_network_refs: [{ get_param: mgmt-net }]
instance_ip_address: ‘192.168.1.4’

## Slide 37: Vip address
Many VMs sharing an IP
To spread the load on multiple devices
Leveraging Contrail ECMP capabilities

## Slide 38: Allowing multiple addresses on a port
192.168.1.13
192.168.1.14
192.168.1.14
192.168.1.14
YES
NO

## Slide 39: Vip means ecmp
VIP configured on the VMI
Need to allow an Allowed Address Pair
Routes automatically added in Contrail
Multiple routes towards the same VIP are seen as ECMP paths

## Slide 40: Allowed address pair
resources:
vmi_1:
type: OS::ContrailV2::VirtualMachineInterface
properties:
name: 'my_vmi'
virtual_network_refs: [{ list_join: [':', { get_attr: [ new_vn, fq_name ] } ] }]
virtual_machine_interface_mac_addresses:
{
virtual_machine_interface_mac_addresses_mac_address: ‘aa:bb:cc:dd:ee:ff’,
}
virtual_machine_interface_allowed_address_pairs:
{
virtual_machine_interface_allowed_address_pairs_allowed_address_pair: [{
virtual_machine_interface_allowed_address_pairs_allowed_address_pair_ip:
{
virtual_machine_interface_allowed_address_pairs_allowed_address_pair_ip_ip_prefix: '192.168.1.100’,
virtual_machine_interface_allowed_address_pairs_allowed_address_pair_ip_ip_prefix_len: '32',
},
virtual_machine_interface_allowed_address_pairs_allowed_address_pair_mac: ‘aa:bb:cc:dd:ee:ff’,
virtual_machine_interface_allowed_address_pairs_allowed_address_pair_address_mode: 'active-active',
}]
}

## Slide 41: Multiple ips on the same mac
Configuration within the VMI object
Add allowed pairs
  MAC address
  IP address
VM vNIC
IP X
MAC Y
AAP 1
MAC Y
IP B
AAP 2
MAC Y
IP D

## Slide 42: Contrail picks the mac
We can avoid to define a custom MAC
Just remove MAC definition and AAP MAC reference
resources:
vmi_1:
type: OS::ContrailV2::VirtualMachineInterface
properties:
name: 'my_vmi'
virtual_network_refs: [{ list_join: [':', { get_attr: [ new_vn, fq_name ] } ] }]
virtual_machine_interface_allowed_address_pairs:
{
virtual_machine_interface_allowed_address_pairs_allowed_address_pair: [{
virtual_machine_interface_allowed_address_pairs_allowed_address_pair_ip:
{
virtual_machine_interface_allowed_address_pairs_allowed_address_pair_ip_ip_prefix: { get_param: '192.168.1.100' },
virtual_machine_interface_allowed_address_pairs_allowed_address_pair_ip_ip_prefix_len: { get_param: '32' },
},
virtual_machine_interface_allowed_address_pairs_allowed_address_pair_address_mode: { get_param: 'active-active' },
}]
}

## Slide 43: Vip in action

## Slide 44: Trunk ports
Multiple vlans inside the VM
Virtual NIC must become a Trunk
Do not Use Openstack Trunk Object
Use Contrail sub-interfaces (which came earlier!)

## Slide 45: How do trunks work?
Concept is easy
Create a parent network
Attach a VMI to it
Create child virtual networks, one for each vlan
Create child VMIs, one for each vlans
Child VMIs must reference the parent VMI
Child VMIs must use parent VMI MAC address
MAC
parent VN
child VN
vlan 100
child VN
vlan 200
parent VMI
child
VMI
child
VMI

## Slide 46: First there is a father
resources:
parent_vn:
type: OS::ContrailV2::VirtualNetwork
properties:
name: { get_param: parent }
network_ipam_refs: ['default-domain:my-project:default-ipam']
network_ipam_refs_data:
[{
network_ipam_refs_data_ipam_subnets:
[{
network_ipam_refs_data_ipam_subnets_subnet:
{
network_ipam_refs_data_ipam_subnets_subnet_ip_prefix: '172.30.1.0',
network_ipam_refs_data_ipam_subnets_subnet_ip_prefix_len: '24',
},
}]
}]
vm_1:
type: OS::Nova::Server
properties:
name: 'trunk_vm'
image: 'vsrx'
flavor: 'vsrx'
networks:
- network: { get_resource: parent_vn }
parent VMI

## Slide 47: Then the children
Child VN is a standard VN
No vlan defined here
No link to parent
child_vn_1:
type: OS::ContrailV2::VirtualNetwork
properties:
name: 'child1'
network_ipam_refs: ['default-domain:my-project:default-ipam']
network_ipam_refs_data:
[{
network_ipam_refs_data_ipam_subnets:
[{
network_ipam_refs_data_ipam_subnets_subnet:
{
network_ipam_refs_data_ipam_subnets_subnet_ip_prefix: '172.30.100.0',
network_ipam_refs_data_ipam_subnets_subnet_ip_prefix_len: '24',
},
}]
}]

## Slide 48: Multiple ports, one mac
Child VMI is where the magic happens
We reference another VMI, the parent
We set the MAC to parent MAC VMI address
We assign the vlan
vmi_1:
type: OS::ContrailV2::VirtualMachineInterface
properties:
name: 'vmi_1'
virtual_network_refs: [{ get_resource: child_vn_1 }]
virtual_machine_interface_properties:
{
virtual_machine_interface_properties_sub_interface_vlan_tag: '100',
}
virtual_machine_interface_mac_addresses:
{
virtual_machine_interface_mac_addresses_mac_address: [{ get_attr: [vm_1, addresses, get_param: 'parent', 0, "OS-EXT-IPS-MAC:mac_addr"] }],
}
virtual_machine_interface_refs: [{ get_attr: [vm_1, addresses, get_param: 'parent', 0, "port"] }]

## Slide 49: How do I get the right mac?
We need to obtain the MAC of the parent
By checking VM attributes
We extract it from ports attributes
Only check on the port connected to the parent network
virtual_machine_interface_mac_addresses:
{
virtual_machine_interface_mac_addresses_mac_address: [{ get_attr: [vm_1, addresses, get_param: 'parent', 0, "OS-EXT-IPS-MAC:mac_addr"] }],
}

## Slide 50: Same old instance ip
Still need the Instance IP
But nothing new here
Same old Instance IP object
iip_1:
type: OS::ContrailV2::InstanceIp
depends_on: [ vmi_1 ]
properties:
virtual_network_refs: [{ get_resource: child_vn_1 }]
virtual_machine_interface_refs: [{ get_resource: vmi_1 }]

## Slide 51: Going out the dc
My Virtual Network needs to leave the DC
In Openstack we have Provider Networks
Here still tenant networks
But we use Route targets
Then same old MP-BGP VPN mechanisms between Contrail and SDN gateway

## Slide 52: Sdn gateway as a pe
Need configuration on SDN gateway as well
We need a VRF
Matching route-target
Usual VRF import/export policies
root@sdn-gw# show routing-instances test_vn
instance-type vrf;
interface lo0.1000;
route-distinguisher 192.168.100.1:1;
vrf-import test_imp;
vrf-export test_exp;
vrf-table-label;

## Slide 53: The right target
Virtual Network can have its own route target
Can import other route-targets
Can export route-targets
resources:
vip_vn:
type: OS::ContrailV2::VirtualNetwork
properties:
name: { get_param: name}
import_route_target_list:
{
import_route_target_list_route_target: [ 'target:65500:131' , 'target:65500:241' ]
}
export_route_target_list:
{
export_route_target_list_route_target: [ 'target:65500:201' ]
}
route_target_list:
{
route_target_list_route_target: ['target:65500:101'],
}

## Slide 54: Bgp as a service
Totally new feature
VMs by default are blind to vRouter networking information
Need to create a communication between vRouter and the VM
This is BGP as a Service (BGPaaS)

## Slide 55: Do you talk bgp?
VM must talk BGP
Session with Virtual Network gateway address
Additional options like prefix limit, as-override, etc…
BGPaaS object references a VMI
…$%!#W@...
[BGP language]

## Slide 56: Customize your bgpaas
bgpaas_2:
type: OS::ContrailV2::BgpAsAService
properties:
name: 'bgp-session-1'
virtual_machine_interface_refs: [{ get_resource: vmi_2 }]
autonomous_system: '65511'
bgpaas_session_attributes:
{
bgpaas_session_attributes_address_families:
{
bgpaas_session_attributes_address_families_family: ['inet','inet6'],
},
bgpaas_session_attributes_family_attributes:
[{
bgpaas_session_attributes_family_attributes_address_family: inet,
bgpaas_session_attributes_family_attributes_loop_count: 1,
bgpaas_session_attributes_family_attributes_prefix_limit:
{
bgpaas_session_attributes_family_attributes_prefix_limit_maximum: 10
}
}]
bgpaas_session_attributes_as_override: 'true'
bgpaas_session_attributes_hold_time: '30'
bgpaas_session_attributes_private_as_action: 'remove'
}

## Slide 57: Neutron vs contrail ?
Neutron objects are available
We can use them with Contrail
Not all Contrail objects are compatible with Contrail

## Slide 58: When do we have to change?
You need additional features that only Contrail can offer
For example, ECMP fields
You need to implement something that, conceptually, is totally different between Contrail and vanilla Neutron
For example, VN that need to go outside the DC

## Slide 59: Lost in translation
We start from a Neutron based template
And need to move to a Contrail based one
We tried to identify some common use-cases
And give best practices on how to transform a stack of Neutron objects in one made with Contrail objects

## Slide 60: Creating services is like a puzzle!

## Slide 61: Basic translation

## Slide 62: Translation #1
Create a VM with one vNIC connected to a new virtual network

## Slide 63: Heat map #1
vmi
instance ip
vm
virtual network

## Slide 64: Translation #2
Create a VM with one vNIC connected to an existing virtual network

## Slide 65: Heat map #2
vmi
instance ip
vm
virtual network

## Slide 66: Translation #3
Create a VM with one vNIC connected to a new virtual network that needs to go outside the DC

## Slide 67: Heat map #3
vmi
instance ip
vm
virtual network
VRF on SDN gateway
matching Route Target

## Slide 68: Translation #4
The VM vNIC needs to be configured as trunk with N vlans

## Slide 69: Heat map #5
parent vmi
child vmi 1
vm
child vn 1
parent vn
child vn N
child vmi N
instance IP 1
instance IP N

## Slide 70: Translation #5
The VM needs to be connected to a L2 network, VXLAN ready

## Slide 71: Heat map #5
vmi
instance ip
vm
virtual network (VXLAN)
EVPN on SDN gateway
matching Route Target

## Slide 72: Translation #6
The virtual network needs to use a custom gw and a custom allocation pool

## Slide 73: Heat map #6
vmi
instance ip
vm
gateway
subnet pool
virtual network

## Slide 74: Translation #7
The VM must have a vNIC with a custom MAC, a fixed IP and must allow the configuration of a VIP address

## Slide 75: Heat map #7
vmi
mac
aap
instance ip
fixed IP
vm
virtual network

## Slide 76: Translation #8
The VM must talk BGP in order to exchange BGP routers and use BFD for faster failure detection

## Slide 77: Heat map #8
vmi
instance ip
vm
virtual network
bgpaas

## Slide 78: Service chaining
Contrail exclusive feature
Manage communications between virtual networks
By adding services between them!

## Slide 79: At first it was two networks
By default two virtual networks cannot talk to each other
They are separate broadcast domain
In a physical network we would need a router

## Slide 80: Then a policy connected them
Networks can talk to each other through a network policy
Applied to both virtual networks
A list of rules telling which traffic can pass or not
Rules built over protocol, dst/src addresses, dst/src virtual networks, dst/src ports

## Slide 81: And a service controlled communications
If policy allows traffic to pass we can add one or more service between the two virtual networks
Service can be a firewall
We bring security between two virtual networks
Service chaining routing is automatically managed by Contrail

## Slide 82: Service chain recipe
Two virtual networks
One network policy applied to those networks
One or more VMs acting as service elements
Service templates describing the nature of the service instance
Port tuple, a collection of ports belonging to a VM
Service instance, the actual service part of the service chain

## Slide 83: Don’t be confused!
Based on the template
Uses ports of a VM as defined in a port tuple
A service instance is not a VM!
We might have multiple service instances using the same VM
NIC1
NIC2
NIC3
NIC4
service instance 1
service instance 2
service template

## Slide 84: Service chain building blocks
Network policy
Service template
Service instance
Port tuple
Modified VMI
Service VM

## Slide 85: Writing your policy
type: OS::ContrailV2::NetworkPolicy
properties:
name: { get_param: pol_name }
network_policy_entries: {
network_policy_entries_policy_rule: [{
network_policy_entries_policy_rule_direction: { get_param: direction },
network_policy_entries_policy_rule_protocol: { get_param: protocol },
network_policy_entries_policy_rule_src_ports: [{
network_policy_entries_policy_rule_src_ports_start_port: { get_param: src_port_start },
network_policy_entries_policy_rule_src_ports_end_port: { get_param: src_port_end }
}],
network_policy_entries_policy_rule_dst_ports: [{
network_policy_entries_policy_rule_dst_ports_start_port: { get_param: dst_port_start },
network_policy_entries_policy_rule_dst_ports_end_port: { get_param: dst_port_end }
}],
network_policy_entries_policy_rule_dst_addresses: [{
network_policy_entries_policy_rule_dst_addresses_virtual_network: { get_param: dst_add }
}],
network_policy_entries_policy_rule_src_addresses: [{
network_policy_entries_policy_rule_src_addresses_subnet: {
network_policy_entries_policy_rule_src_addresses_subnet_ip_prefix: {get_param: rule_cidr_1},
network_policy_entries_policy_rule_src_addresses_subnet_ip_prefix_len: {get_param: rule_mask_1},
}
}],
network_policy_entries_policy_rule_action_list: {
network_policy_entries_policy_rule_action_list_simple_action: { get_param: simple_action },
network_policy_entries_policy_rule_action_list_apply_service: [{ get_param: svc_inst_fq_name }]
},
}]
}

## Slide 86: Applying policy to a virtual network
Policy must be assigned to virtual networks too
To both virtual networks, left and right
left_vn:
type: OS::ContrailV2::VirtualNetwork
depends_on: [ net_policy_apn_1 ]
properties:
...
network_policy_refs: [{ get_param: pol_fq_name }]
network_policy_refs_data:
[{
network_policy_refs_data_sequence:
{
network_policy_refs_data_sequence_major: 0,
network_policy_refs_data_sequence_minor: 0,
},
}]

## Slide 87: Draw your template
Defines service characteristics
Type, mode, interfaces
svc_tmplt:
type: OS::ContrailV2::ServiceTemplate
properties:
name: { get_param: service_template_name }
service_template_properties:
{
service_template_properties_version: '2',
service_template_properties_service_mode: 'in-network',
service_template_properties_service_type: 'firewall',
service_template_properties_interface_type:
[
{
service_template_properties_interface_type_service_interface_type: 'left',
},
{
service_template_properties_interface_type_service_interface_type: 'right',
}
],
service_template_properties_ordered_interfaces: 'true',
}
domain: 'default-domain'

## Slide 88: Define the service instance
We bind interfaces to virtual networks
svc_inst_apn_1:
type: OS::ContrailV2::ServiceInstance
depends_on: [ svc_tmplt ]
properties:
name: { get_param: svc_inst_name }
service_instance_properties:
{
service_instance_properties_interface_list:
[
{
service_instance_properties_interface_list_virtual_network:
{
list_join: [':', { get_attr: [ left_vn, fq_name ] } ]
},
},
{
service_instance_properties_interface_list_virtual_network:
{
list_join: [':', { get_attr: [ right_vn, fq_name ] } ]
},
}
],
}
service_template_refs: [{ get_resource: svc_tmplt }]

## Slide 89: Gather ports into a tuple
Binds a list of interfaces
References a service instance
prt_tpl_1:
type: OS::ContrailV2::PortTuple
depends_on: [ svc_inst_apn_1 ]
properties:
name: { get_param: tuple_name }
service_instance: { list_join: [':', { get_attr: [ svc_inst_apn_1, fq_name ] } ] }
vmi_2:
type: OS::ContrailV2::VirtualMachineInterface
depends_on: [ prt_tpl_1 ]
properties:
virtual_machine_interface_properties:
{
virtual_machine_interface_properties_service_interface_type: 'left',
}
port_tuple_refs: [{ get_resource: prt_tpl_1 }]
virtual_network_refs: [{ list_join: [':', { get_attr: [ left_vn, fq_name ] } ] }]

## Slide 90: Service vm will manage traffic
Standard VM
Some of its ports assigned to the service instance
vm1:
type: OS::Nova::Server
depends_on: [ iip_1, iip_2, iip_3 ]
properties:
name: {get_param: vm1name }
image: { get_param: image }
flavor: { get_param: flavor }
networks:
- port: { get_resource: vmi_1 }
- port: { get_resource: vmi_2 }
- port: { get_resource: vmi_3 }
instance
VM
left
right

## Slide 91: Service chaining heat map
left vn
right vn
policy
service instance
service template
port tuple
VM
x3 vmi
x3 instance IP

## Slide 92: Use cases? Sky is the limit
Policy allows inter-VN communication
Service configured between the two VN
Service Firewall blocks some traffic!

## Slide 93: Summing up
SDN brings automation
Automation in Openstack means Heat
Contrail has its own Heat objects
Models to create VNFs with Contrail
Best practices to translate Neutron templates to Contrail templates

## Slide 94
That’s all!